## Slide 1
Acid Rain
Demonstrating the acid rain phenomenon

## Slide 2
Acid Rain
Demonstrating the acid rain phenomenon
Objective
The purpose of this activity is to investigate the effect of acid rain forerunner on water acidity, create a hypothesis and proceed to test it using the Labidsc pH-meter sensor.

## Slide 3
In our modern society we rely on the use of fossil fuels in numerous aspects of our daily life, for example to operate vehicles, produce electricity, heating, industry and much more. A large amount of particulate pollutants are released into the atmosphere because of the combustion of these types of fuels. This contamination can be transported long distances by wind or become concentrated in defined spaces.
Introduction and theory
Acid Rain
Demonstrating the acid rain phenomenon

## Slide 4
Have you ever seen or heard about the grey layer above some cities called smog?
What environmental effects are produced by gas emission from fossil fuel combustion?
What directly determines the pH of acid rain?
Introduction and theory
Acid Rain
Acid Rain
Demonstrating the acid rain phenomenon
Carry out the experiment activity with your class so that at the end you’ll be able to answer the following question:

## Slide 5
Theoretical
The gases (nitrogen oxides, sulfur dioxide and carbon dioxide) produced by fossil fuels burning mainly react in the atmosphere with water and oxygen. The result is an acid solution which when it falls as water is called acid rain. Deposition of these compounds also occurs in wet environments where fog is present.
Acid rain mainly affects watershed ecosystems. The majority of lakes and streams have a pH between six and eight, a range essential to sustain an appropriate habitat for plants and animals. Many water bodies are seriously affected because the basin soils are unable to neutralize new loads of acidity.
The addition of acidic compounds to ground and water has a direct impact on plants and animals.
Introduction and theory
Acid Rain
Demonstrating the acid rain phenomenon

## Slide 6
Introduction and theory
Many forests are highly sensitive to acid variation from soil and air humidity, resulting in detrimental effects such as the direct destruction of leaf tissue and even reduced growth of roots. Animals, fish and amphibians are affected mainly at the primary and juvenile stages with data showing that at pH 5 the majority of fish eggs cannot hatch and at lower pH adults die.
Acid rain also accelerates the decay of buildings of all types, which is of particular loss to mankind when culturally relevant sculptures and architectural monuments are affected.
Acid Rain
Demonstrating the acid rain phenomenon

## Slide 7
Introduction and theory
Now students are encouraged to raise a hypothesis which must be tested with an experiment.
How will the water pH change by direct CO2 exposure?
Acid Rain
Demonstrating the acid rain phenomenon

## Slide 8
Activity description
Students will study the variation of water acidity due to carbon dioxide dissolution. They will blow into a volume of water with a straw and visualize their results in real time using GlobiLab software. After that, they will use tools for graph analysis to find out the results.
Acid Rain
Demonstrating the acid rain phenomenon

## Slide 9
Labdisc Biochem
Beaker
pH-meter
Straw
Distilled water
Resources and materials
1
2
3
1
3
2
4
Acid Rain
Demonstrating the acid rain phenomenon
4
5

## Slide 10
Using the Labdisc
To collect measurements with the Labdisc and pH sensor, the Labdisc must be configured according to the following steps:
Open the GlobiLab software and turn on the Labdisc
Click on the Bluetooth icon in the bottom right corner of the GlobiLab screen. Select the Labdisc you are using currently. Once the Labdisc has been recognized by the software, the icon will change from a grey to blue color . If you prefer a USB connection follow the previous instruction clicking on the USB icon. You will see the same color change when the Labdisc is recognized .
1
2
Labdisc configuration
Acid Rain
Demonstrating the acid rain phenomenon

## Slide 11
Click on to configure the Labdisc. Select pH in the “Logger Setup” window. Enter “1/Sec” for the sampling Rate and “1000” for Samples.
3
Using the Labdisc
Acid Rain
Demonstrating the acid rain phenomenon

## Slide 12
Once you have finished the sensor configuration start measuring by clicking
Once you have finished measuring stop the Labdisc by clicking
4
5
Using the Labdisc
Acid Rain
Demonstrating the acid rain phenomenon

## Slide 13
Experiment
Pour 50 mL. of distilled water in the beaker.
Enter the pH sensor without touching the sides or bottom of the beaker.
Start measurements and record the initial pH for a few seconds.
Blow into the water with the straw for one minute.
Continue measuring for one minute and then, stop Labdisc.
1
2
Acid Rain
Demonstrating the acid rain phenomenon
3
4
5

## Slide 14
Results and analysis
Select a line graph from the GlobiLab menu to show the experiment results.
Then, label parts of the curve according to the experimental stages with the tool.
After that, show pH values from the initial and final states with the markers, by clicking on every section.
1
2
3
Acid Rain
Demonstrating the acid rain phenomenon

## Slide 15
Results and analysis
Was your hypothesis proved? Explain.
What effect was caused by blowing air into the water?
What happened to the pH change when you stopped blowing?
Acid Rain
Demonstrating the acid rain phenomenon

## Slide 16
Results and analysis
The graph below should be similar to the one the students came up with:
Acid Rain
Demonstrating the acid rain phenomenon

## Slide 17
Conclusion
What does the pH decrement depend on?
Students should point out that the pH decreases due to dissolution of carbon dioxide in water. The pH decrement is directly related to available CO2 which depends on the time spent blowing into the water.
Why didn’t the pH reach the original value after the experiment?
Students should infer from the experiment that the dissolved carbon dioxide reacts to water and oxygen which comes from the blown air producing a carbonic acid solution. They could support their proposals by going over the theoretical background.
Acid Rain
Demonstrating the acid rain phenomenon

## Slide 18
Conclusion
How can you relate this experiment to what happen on Earth?
Students should indicate that the acidification of water due to dissolved CO2 as a result of the experiment is similar to atmospheric dissolution of industrial gases. It is important to relate the acidity degree to the concentration of this kind of pollution.
Acid Rain
Demonstrating the acid rain phenomenon

## Slide 19
Activities for further application
How would you evaluate the atmospheric contamination level in your city?
Students could propose to collect some samples of rain over winter in their city and measure the water acidity. They should plan to compare the pH values between the first rain after a long dry period and the next water samples.
What actions could help with the prevention of acid rain?
Students could suggest limiting the amount of industrial emissions and promote alternative energy sources. They also could indicate individual actions, such as cleaning smokestacks and pipes, turning devices off when they are not in use, better insulating homes to avoid excessive heating or cooling system use and more.
Acid Rain
Demonstrating the acid rain phenomenon